## Slide 1: Thorium
Hardware test automation that fails at compile time
Thomas Rambrant · Knowit Connectivity

## Slide 2: A test rig fails in expensive ways
The problem

## Slide 3: Four ways a test suite lies to you
The problem
A mistyped test point measures the wrong pin — and passes
A criterion compared against the wrong unit — and passes
A relay path nobody wired up — throws three hours into a soak test
A tolerance table edited for one variant, not the others
Every one of these is a static fact.
None of them needs a running rig to discover.

## Slide 4
If a mistake can be caught by the compiler,
it must be caught by the compiler.
Runtime checks are a last resort — and each one is a documented concession.

## Slide 5: A test script reads like the test specification
How it works

## Slide 6: What a script never mentions
How it works
The whole test
auto rail = Measure(
Dmm1.voltage(),
at( DeviceX::Output5V));
Verify(
FS_Supply_1::FS_Supply_5V0,
rail);
Nowhere in it
Instrument address
Relay path or channel numbers
Unit conversion
Tolerance value
A single logging call
All resolved elsewhere — most of it by the compiler.

## Slide 7: Four sources of truth
How it works
rig/ which instruments this bench has, and how they are wired
dut/ named test points and tolerance tables
suite/ the test scripts and the catalog that lists them
libs/ the portable framework — knows nothing about either
A second bench testing a second device is its own repository.
It reuses libs/ untouched and brings its own three.

## Slide 8: Fourteen mistakes that now fail the build
The payoff

## Slide 9: What the compiler now refuses
The payoff
A misspelled test point
A misspelled criterion
A criterion in the wrong unit
A test point nobody wired up
A tolerance variant missing a limit
A renamed script in the catalog
Connecting a supply with no relay
Channel 5 on a 4-channel scope
A driver with no safe state
A half-declared unit
…and four more
Seconds, on a laptop — not hours, on the bench.

## Slide 10: Two checks worth a closer look
The payoff
Wiring coverage. One test file has no assertions at all — the point is that it compiles. It walks every declared test point and demands a matching wiring entry. Forget one and the build stops.
Tolerance variants. Production, stress-chamber and aged-equipment limits are three tables. A value unchanged from production is written once and referenced — so it cannot drift, and a typo in the reference will not compile.

## Slide 11: Every run explains itself, twice
Evidence

## Slide 12: One event stream, two audiences
Evidence
For people
Colour-coded RTF, opens in Word
Grouped the way the catalog is
Each check states what was measured and what was required
Readable while the run is going
Live on the console too
For tools
SARIF 2.1.0 — an industry format
Every step, routing and safing
Each requirement becomes a queryable rule
Ingested by CI, no custom parser

## Slide 13: Both logs answer: which run?
Evidence
Device and serial number · operator · tolerance table
Framework version · revision of the scripts, device and rig data
The command line · local time for a person, UTC for a machine
Stamped in by the build, not typed in by a caller — so a report cannot claim the wrong device or the wrong limits.

## Slide 14: 278 tests, and none of them need a rig
Evidence
Test scripts run with readings injected, or replayed from a real run
Two test targets exist only to fail the build on inconsistent data
Seventeen acceptance tests drive the real binary as a subprocess and keep every log they produce
A developer can change the framework and know within seconds whether a bench would still behave.

## Slide 15: What this buys, and what it costs
Honestly

## Slide 16: Pros and cons
Honestly
Strengths
Whole classes of mistake cannot reach the bench
Scripts trace straight to the spec
Operator view and machine record cannot disagree
Scripts testable with no hardware
One tolerance value, three tables
Reusable across benches
Costs and risks
Experimental C++26; GCC 16 only
New scripts need a developer, not a spreadsheet
Wiring changes mean a rebuild
Few engineers have used reflection
Instrument drivers still simulated
Template errors can be verbose

## Slide 17: Done, and open
Honestly
Working today. Units and tolerances, routed measurements, a switching fabric, safing, three tolerance variants, session injection and replay, both log streams, the catalog runner and its CLI.
Next. A real instrument transport. Moving the remaining runtime wiring check to compile time. Deciding whether a second bench is a fork or a package.

## Slide 18: In closing
The rig should never find your mistake first.
  The compiler is cheaper, faster and more thorough than a bench — so everything that can be decided before power-on, is.